## Slide 1: Computer Architecture
Processor Design: Datapath and Control
Slides are derived from work by Daniel J. Sorin (Duke), Amir Roth (Penn)

## Slide 2: This Unit: Processor Design
Datapath components and timing
  Registers and register files
  Memories (RAMs)
Mapping an ISA to a datapath
Control
Exceptions
Application
OS
Firmware
Compiler
CPU
I/O
Memory
Digital Circuits
Gates & Transistors

## Slide 3: So You Have an ALU…
Important reminder: a processor is just a big finite state machine (FSM) that interprets some ISA
Start with one instruction
add $3,$2,$4
  ALU performs just a small part of execution of instruction
  You have to read and write registers
  You have have to fetch the instruction to begin with
What about loads and stores?
  Need some sort of memory interface
What about branches?
  Need some hardware for that, too

## Slide 4: Datapath and Control
PC
Insn
memory
Register File
Data Memory
control
Datapath: registers, memories, ALUs (computation)
Control: which registers read/write, which ALU operation
Fetch: get instruction, translate into control
Processor Cycle: Fetch  Decode  Execute
datapath
fetch

## Slide 5: Building a Processor for an ISA
Fetch is pretty straightforward
  Just need a register (called the Program Counter or PC) to hold the
next address to fetch from instruction memory
  Provide address to instruction memory  instruction memory provides instruction at that address
Let’s start with the datapath
Look at ISA
Make sure datapath can implement every instruction

## Slide 6: Datapath for MIPS ISA
Consider only the following instructions
add $1,$2,$3
addi $1,$2,<value> lw $1,4($3)
sw $1,4($3)
beq $1,$2,PC_relative_target j Absolute_target
Why only these?
  Most other instructions are similar from datapath viewpoint
  I leave the ones that aren’t for you to figure out

## Slide 7: Review: A Register
Register: DFF array with shared clock, write-enable (WE)
  Notice: both a clock and a WE (DFFWE = clock & registerWE)
  Convention I: clock represented by wedge
  Convention II: if no WE, DFF is written on every clock
DFF
DFF
DFF
D0
D1
DN-1
WE CLK
Q0
Q1
QN-1
D
Q
N
N
WE
D Q
32 bit reg
E Q
Note: Above is the “classic” register we learned before; we’re just introducing a new symbol for the same thing
=

## Slide 8: Uses of Registers
PC
Insn
memory
Register File
Data Memory
control
A single register is good for some things
  PC: program counter
  Other things which aren’t the ISA registers (more later in semester)
datapath
fetch

## Slide 9: What About the ISA Registers?
Register file: the ISA (“architectural”, ”visible”) registers
  Two read “ports” + one write “port”
    Maximum number of reads/writes in single instruction (R-type)
Port: wires for accessing an array of data
  Data bus: width of data element (MIPS: 32 bits)
  Address bus: width of log2 number of elements (MIPS: 5 bits)
  Write enable: if it’s a write port
  M ports = M parallel and independent accesses
Register File
RS2VAL
RDVAL
RD = dest reg RS = source reg
Write Enable
32
RS1VAL
32
5 5 5
WE RD RS1 RS2
Write port
Read port 1
Read port 2

## Slide 10: Register File With Tri-State Read Ports
RS2
RS1
RD
WE
RDVAL
RS2VAL
RS1VAL

## Slide 11: Another Useful Component: Memory
Memory
DATAOUT
DATAIN
WE
Memory: where instructions and data reside
  One read/write “port”: one access per cycle, either read or write
    One address bus
  One input data bus for writes, one output data bus for reads
Actually, a more traditional definition of memory is
  One input/output data bus
  No clock  asynchronous “strobe” instead
ADDRESS

## Slide 12: Dramatis Personae
14
P C
Register
Mem
Memory
Register
File
rs1 rs2 rd
RDVAL
s1VAL
s2VAL
WE
Register File
ALU
In1
In2
Result
ALUop
(Which math to do)
Arithmetic Logic Unit
<< 2
Shift left by two bits
+
Adder
+
4
Adder that always adds 4
Sign extender
S
X
Converts to longer bit widths; preserves sign
(3) 0011 => 00000011 (still 3)
(-7) 1001 => 11111001 (still -7)
Mux
In1
In2
Which?
Result
Plain ol’ AND gate
Zero extender
0
X
Converts to longer bit widths for unsigned numbers
(3) 0011 => 00000011 (still 3)
(9) 1011 => 00001001 (still 9)

## Slide 13: Let’s Build A MIPS-like Datapath

## Slide 14: Start With Fetch
PC and instruction memory
A +4 incrementer computes default next instruction PC
  Why +4 (and not +1)? What will it be for 16-bit Duke 250/16?
P
C
Insn
Mem
+ 4

## Slide 15: First Instruction: add $rd, $rs, $rt
Add register file and ALU
P
C
Insn
Mem
Op(6) | rs(5) | rt(5) | rd(5)
Sh(5)
Func(6)
R-type
Register
File
s1 s2 d
+ 4
rs
rt
rs + rt

## Slide 16: Second Instruction: addi $rt, $rs, imm
P
C
Insn
Mem
S X
I-type
Destination register can now be either rd or rt
Add sign extension unit and mux into second ALU input
Op(6) | rs(5) | rt(5) | Immed(16)
Register
File
s1 s2 d
+ 4
rs
Extended(imm)
sign extension (sx) unit
16
32

## Slide 17: Third Instruction: lw $rt, imm($rs)
P
C
Insn
Mem
S X
I-type
Add data memory, address is ALU output (rs+imm)
Add register write data mux to select memory output or ALU output
Op(6) | rs(5) | rt(5) | Immed(16)
Register
File
s1 s2 d
a
Data
d Mem
+ 4

## Slide 18: Fourth Instruction: sw $rt, imm($rs)
P
C
Insn
Mem
S X
I-type
Add path from second input register to data memory data input
Disable RegFile’s WE signal
Op(6) | rs(5) | rt(5) | Immed(16)
Register
File
s1 s2 d
a
Data
d Mem
+ 4
?

## Slide 19: Fifth Instruction: beq $1,$2,target
P
C
Insn
Mem
S X
I-type
Add left shift unit (why?) and adder to compute PC-relative branch target
Add mux to do what?
Op(6) | rs(5) | rt(5) | Immed(16)
Register
File
s1 s2 d
a
Data
d Mem
+ 4
<< 2
+
z

## Slide 20: Sixth Instruction: j
Add shifter to compute left shift of 26-bit immediate
Add additional PC input mux for jump target
P
C
Insn
Mem
S X
Op(6)
J-type
Immed(26)
Register
File
s1 s2 d
a
Data
d Mem
+ 4
<< 2
+
0
X
26
32
<<
2

## Slide 21: Seventh, Eight, Ninth Instructions
Are these the paths we would need for all instructions?
sll $1,$2,4 // shift left logical
  Like an arithmetic operation, but need a shifter too
slt $1,$2,$3 // set less than (slt)
  Like subtract, but need to write the condition bits, not the result
    Need zero extension unit for condition bits
    Need additional input to register write data mux
jal absolute_target // jump and link
  Like a jump, but also need to write PC+4 into $ra ($31)
    Need path from PC+4 adder to register write data mux
    Need to be able to specify $31 as an implicit destination
jr $31 // jump register
  Like a jump, but need path from register read to PC write mux

## Slide 22: Clock Timing
24
Must deliver clock(s) to avoid races
Can’t write and read same value at same clock edge
  Particularly a problem for RegFile and Memory
May create multiple clock edges (from single input clock) by using buffers (to delay clock) and inverters
For Homework 4 (the Duke 250/16 CPU):
  Keep the clock SIMPLE and GLOBAL
  You may need to do the PC on falling edge and everything else on
rising edge
    Changing clock edges in this way will separate PC++ from logic
    Otherwise, if the PC changes while the operation is occurring, the instruction bits will change before the answer is computed -> non-deterministic behavior 
    Note: A cheap way to make something trigger on the other clock
edge is to NOT the clock on the way into that component

## Slide 23: This Unit: Processor Design
Datapath components and timing
  Registers and register files
  Memories (RAMs)
  Clocking strategies
Mapping an ISA to a datapath
Control
Exceptions
Application
OS
Firmware
Compiler
CPU
I/O
Memory
Digital Circuits
Gates & Transistors

## Slide 24: What Is Control?
P
C
Insn
Mem
S X
Register
File
s1 s2 d
a
Data
d Mem
+ 4
<< 2
Rwe
DMwe
JP
ALUop
BR
Rwd
Rdst ALUinB
9 signals control flow of data through this datapath
  MUX selectors, or register/memory write enable signals
  Datapath of current microprocessor has 100s of control signals
0
X
<<
2

## Slide 25: Example: Control for add
P
C
Insn
Mem
S X
Register
File
s1 s2 d
a
Data
d Mem
+ 4
<< 2
BR=0
JP=0
Rwd=0
ALUop=0DMwe=0
ALUinB=0
Rdst=1
Rwe=1
Rwe: Register Write Enable
Rdst: Register Destination chooser
ALUinB: ALU input B chooser
ALUop: ALU operation (multi-bit)
DMwe: Data Memory Write Enable
Rwd: Register Write Data chooser
BR: Branch?
JP: Jump?
0
X
<<
2

## Slide 26: Example: Control for sw
P
C
Insn
Mem
S X
Register
File
s1 s2 d
a
Data
d Mem
+ 4
<< 2
Rwe=
0
=1
DMwe
=1
JP
=0
ALUop
=0
BR
=0
Rwd
=X
Rdst ALUinB
Difference between a sw and an add is 5 signals
  3 if you don’t count the X (“don’t care”) signals
=X
0
X
<<
2

## Slide 27: Example: Control for sw
Difference between a sw and an add is 5 signals
  3 if you don’t count the X (“don’t care”) signals
P
C
Insn
Mem
S X
Register
File
s1 s2 d
a
Data
d Mem
+ 4
<< 2
Rwe=0
JP=0
ALUop=0DMwe=1
ALUinB=1
BR=0
Rwd=X
Rdst=X
0
X
<<
2

## Slide 28: Example: Control for beq $1,$2,target
Difference between a store and a branch is only 4 signals
P
C
Insn
Mem
S X
Register
File
s1 s2 d
a
Data
d Mem
+ 4
<< 2
Rwe=0
JP=0
ALUop=1DMwe=0
ALUinB=0
BR=1
Rwd=X
Rdst=X
0
X
<<
2

## Slide 29: How Is Control Implemented?
P
C
Insn
Mem
S X
Register
File
s1 s2 d
a
Data
d Mem
+ 4
<< 2
Rwe
DMwe
JP
ALUop
BR
Rwd
Rdst ALUinB
Control?
0
X
<<
2

## Slide 30: Implementing Control
Each instruction has a unique set of control signals
  Most signals are function of opcode
  Some may be encoded in the instruction itself
    E.g., the ALUop signal is some portion of the MIPS Func field
+ Simplifies controller implementation
– Requires careful ISA design
Options for implementing control
  Use instruction type to look up control signals in a table
  Design combinational logic whose outputs are control signals
    Either way, goal is same: turn instruction into control signals

## Slide 31: Control Implementation: ROM
ROM (read only memory): like a RAM but unwritable
  Bits in data words are control signals
  Lines indexed by opcode
Example: ROM control for our simple datapath
 | BR | JP | ALUinB | ALUop | DMwe | Rwe | Rdst | Rwd
add | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
addi | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0
lw | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
sw | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0
beq | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
j | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
opcode

## Slide 32: ROM vs. Combinational Logic
A control ROM is fine for 6 insns and 9 control signals
A real machine has 100+ insns and 300+ control signals
  Even “RISC”s have lots of instructions
  30,000+ control bits (~4KB)
Not huge, but hard to make fast
  Control must be faster than datapath
Alternative: combinational logic
  It’s that thing we know how to do! Nice!
  Exploits observation: many signals have few 1s or few 0s

## Slide 33: Control Implementation Combinational Logic with a Decoder (one-hot representation)
ALUinB
Example: combinational logic control for our simple datapath
opcode add addi lw sw beq j
BR
JP DMwe
Rwd
Rdst
ALUop
Rwe

## Slide 34: This Unit: Processor Design
Datapath components and timing
  Registers and register files
  Memories (RAMs)
  Clocking strategies
Mapping an ISA to a datapath
Control
Exceptions
Application
OS
Firmware
Compiler
CPU
I/O
Memory
Digital Circuits
Gates & Transistors

## Slide 35: Exceptions
Exceptions and interrupts
  Infrequent (exceptional!) events
    I/O, divide-by-0, illegal instruction, page fault, protection fault, ctrl- C, ctrl-Z, timer
  Handling requires intervention from operating system
    End program: divide-by-0, protection fault, illegal insn, ^C
    Fix and restart program: I/O, page fault, ^Z, timer
  Handling should be transparent to application code
    Don’t want to (can’t) constantly check for these using insns
    Want “Fix and restart” equivalent to “never happened”

## Slide 36: Exception Handling
What does exception handling look like to software?
  When exception happens…
  Control transfers to OS at pre-specified exception handler address
  OS has privileged access to registers user processes do not see
    These registers hold information about exception
    Cause of exception (e.g., page fault, arithmetic overflow)
    Other exception info (e.g., address that caused page fault)
    PC of application insn to return to after exception is fixed
  OS uses privileged (and non-privileged) registers to do its “thing”
  OS returns control to user application
Same mechanism available programmatically via SYSCALL

## Slide 37: MIPS Exception Handling
MIPS uses registers to hold state during exception handling
  These registers live on “coprocessor 0”
  $14: EPC (holds PC of user program during exception handling)
  $13: exception type (SYSCALL, overflow, etc.)
  $8: virtual address (that produced page/protection fault)
  $12: exception mask (which exceptions trigger OS)
Exception registers accessed using two privileged
instructions mfc0, mtc0
  Privileged = user process can’t execute them
  mfc0: move (register) from coprocessor 0 (to user reg)
  mtc0: move (register) to coprocessor 0 (from user reg)
Privileged instruction rfe restores user mode
  Kernel executes this instruction to restore user program

## Slide 38: MIPS Exception Handling
MIPS uses registers to hold state during exception handling
  These registers live on “coprocessor 0”
  $14: EPC (holds PC of user program during exception handling)
  $13: exception type (SYSCALL, overflow, etc.)
  $8: virtual address (that produced page/protection fault)
  $12: exception mask (which exceptions trigger OS)
Exception registers accessed using two privileged
instructions mfc0, mtc0
  Privileged = user process can’t execute them
  mfc0: move (register) from coprocessor 0 (to user reg)
  mtc0: move (register) to coprocessor 0 (from user reg)
Privileged instruction rfe restores user mode
  Kernel executes this instruction to restore user program

## Slide 39: Implementing Exceptions
Why do architects care about exceptions?
  Because we use datapath and control to implement them
  More precisely… to implement aspects of exception handling
    Recognition of exceptions
    Transfer of control to OS
    Privileged OS mode
Later in semester, we’ll talk more about exceptions (b/c we
need them for I/O)

## Slide 40: Datapath with Support for Exceptions
Co-processor register (CR) file needn’t be implemented as RF
  Independent registers connected directly to pertinent muxes
PSR (processor status register): in privileged mode?
S X
Register File
s1 s2 d
a
Data
Mem
d
+ 4
<<
2
<< 2
P Insn I
C Mem R
B
A
O
D
Co-procesor Register File
P
S
R
ALUinAC
PCwC
CRwd
CRwe
PSRs
PSRr

## Slide 41: Summary
We now know how to build a fully functional processor
But …
  We’re still treating memory as a black box (actually two green boxes, to
be precise)
  Our fully functional processor is slow. Really, really slow.

## Slide 42: “Single-Cycle” Performance
Useful metric: cycles per instruction (CPI)
+ Easy to calculate for single-cycle processor: CPI = 1
  Seconds/program = (insns/program) * 1 CPI * (N seconds/cycle)
  ICQ: How many cycles/second in 3.8 GHz processor?
Slow!
  Clock period must be elongated to accommodate longest operation
    In our datapath: lw
    Goes through five structures in series: insn mem, register file (read), ALU, data mem, register file again (write)
  No one will buy a machine with a slow clock
    Not even your grandparents!
  Biggest issue: data memory itself is sloooooooooooooooooooooooow
Next up: Speed up data memory!
Later on: Faster processor cores!

## Slide 43: This Unit: Processor Design
Datapath components and timing
  Registers and register files
  Memories (RAMs)
  Clocking strategies
Mapping an ISA to a datapath
Control
Application
OS
Firmware
Compiler
CPU
I/O
Memory
Digital Circuits
Gates & Transistors
Next up: Memory Systems